## Slide 1
Safety instruction
19th January 2015
Handling of
Hazardous substances
Department Keimer
________________________________________________________________________________________________________________________
Safety Specialists FKF: Michael Wied, Bernhard Fenk, Martin Siemers

## Slide 2
________________________________________________________________________________________________________________________
Safety Specialists FKF: Michael Wied, Bernhard Fenk, Martin Siemers
Explosive
Oxidizing
Flammable
Very toxic
Toxic
Corrosive
Sensitizing
Carcinogenic
Toxic for reproduction
Mutagenic
Dangerous for the environment
Compressed gases
Hazardous substances are substances or preparations that have one or more hazardous characteristics
In total there are 29 hazard classes, among others:
Definition – hazardous substances

## Slide 3
________________________________________________________________________________________________________________________
Safety Specialists FKF: Michael Wied, Bernhard Fenk, Martin Siemers
Possibilities of substitution according GefstoffV §6 paragraph 1 sentence 2 number 4, GefstoffV §7 paragraph 3, TRGS 600
Inform yourself before handling hazardous substances about:
  risks, dangers,
  protective measures,
  proper disposal and
  behavior in emergency situations
Development of gases, vapors etc. has to be avoided
Contact with hazardous substances has to be avoided
Use suitable personal protective equipment
General procedures for handling of hazardous substances

## Slide 4
________________________________________________________________________________________________________________________
Safety Specialists FKF: Michael Wied, Bernhard Fenk, Martin Siemers
Hygienic measures for handling of hazardous substances
Foodstuffs, drinks and tobacco must be stored separately from hazardous substances
The consumption of food and beverages in chemical
laboratories is prohibited
After work and before breaks hands should be washed thoroughly
Lab coats must be cleaned regularly and must be exchanged for clean
ones
!
!
!
!
Don’t store liquid hazardous substances in beverage bottles
!
Remove splashes of hazardous substances on the skin
immediately
!
Remove contaminations on lab desks or on equipments immediately with appropriate cleaning agents !!!!
!

## Slide 5
________________________________________________________________________________________________________________________
Safety Specialists FKF: Michael Wied, Bernhard Fenk, Martin Siemers
Personal Protective Equipment for handling of hazardous substances
Use safety gloves, if activities might lead to mechanical skin irritations (e.g. activities with fibers, mineral wool by oven building etc.)
Use eye and face protection, with: • defined hazardous substances (e.g. acids, solvents) • working over head • Activities with high formation of dust • Activities with danger of splashing (Eye bath must be available)
Use appropriate safety gloves, while working with hazardous substances, especially with acids/lyes or solvents
Use foot protection when carrying heavy parts

## Slide 6
________________________________________________________________________________________________________________________
Safety Specialists FKF: Michael Wied, Bernhard Fenk, Martin Siemers
Basic requirement for safe handling of hazardous substances
  Order and cleanliness in the lab must be observed
Waste materials must be disposed of immediately
  Danger by spilled hazardous substances
Clean work area only with appropriate cleaning aids
  Use of appropriate binding agents
  Avoid to raise dust
Store hazardous substances only in designated rooms
  Safety cabinet
Order and cleanliness in the laboratory

## Slide 7
________________________________________________________________________________________________________________________
Safety Specialists FKF: Michael Wied, Bernhard Fenk, Martin Siemers
Order and cleanliness in the laboratory

## Slide 8
Possibilities of substituting Methanol by Ethanol
________________________________________________________________________________________________________________________
Safety Specialists FKF: Michael Wied, Bernhard Fenk, Martin Siemers
Check if it is possible to replace Methanol by Ethanol
 | Naturlatex Conform+ Break through time [min] | Nitril Touch‘n‘ Tuff Break through time [min] | Nitril Sol-Vex Break through time [min] | Neopren DermaShield Break through time [min] | PE Barrier Break through time [min]
Methanol | < 10 | 1 | 127 | 18 | > 480
Ethanol | < 10 | 8 | 240-480 | 30-60 | > 480
Example: cleaning equipment with Methanol or Ethanol
Vapor pressure 130,3 hPa at 20,0 °C
(Methanol)
Vapor pressure 59,5 hPa at 20,0 °C
(Ethanol)
Methanol has a higher vapor pressure and will be easily breathed in
Methanol penetrates glove material more rapidly than Ethanol

## Slide 9
Hazards of Methanol compared with hazards of Ethanol
________________________________________________________________________________________________________________________
Safety Specialists FKF: Michael Wied, Bernhard Fenk, Martin Siemers
Methanol
Ethanol
H225
Highly flammable liquid and vapor.
H301 + H311 + H331
Toxic if swallowed, in contact with skin
or if inhaled
H370
Causes damage to organs.
H225
Highly flammable liquid and vapor.

## Slide 10
Suitable lab clothes
________________________________________________________________________________________________________________________
Safety Specialists FKF: Michael Wied, Bernhard Fenk, Martin Siemers
Change and new lab coats:
Room 2 M 10;
Mo, We, Fr 9:30 am. – 11:30 am.
Mandatory to wear while working with chemicals
and not in offices / rest areas
(Carry-over of hazardous materials, also possible by gloves!)
long trouser, lab coat, closed toed shoes, suitable PPE
!
!
Not this way!

## Slide 11
GHS – Simplified labeling in laboratories
Proposal of the AK Laboratories for the in-
house labeling of lab-jars
Name of substance
Hazard pictogram on adhesive label
Short version of H-Statement below the pictogram
Priority rule with at most 3 pictograms
GHS09 must not be used
GHS – Simplified labeling in laboratories
________________________________________________________________________________________________________________________
Safety Specialists FKF: Michael Wied, Bernhard Fenk, Martin Siemers

## Slide 12
GHS – Simplified labeling in laboratories
GHS – Simplified labeling in laboratories
________________________________________________________________________________________________________________________
Safety Specialists FKF: Michael Wied, Bernhard Fenk, Martin Siemers

## Slide 13
Simplified labeling for products for scientific research
No test data? Handle like:
Acute Toxicity Cat. 3 (H331, H311, H301)
Skin irritation Cat. 2 (H315)
Mutagenicity Cat. 2 (H341)
Skin sensitizer Cat. 1 (H317)
GHS – Simplified labeling in laboratories
GHS – Simplified labeling in laboratories
Untested
research
substance
________________________________________________________________________________________________________________________
Safety Specialists FKF: Michael Wied, Bernhard Fenk, Martin Siemers

## Slide 14
Questions?
________________________________________________________________________________________________________________________
Safety Specialists FKF: Michael Wied, Bernhard Fenk, Martin Siemers